## Slide 1: CS 2200 Interrupts, Traps, and Exceptions

## Slide 2: How useful is our datapath so far?
No way to do I/O
No way to detect or handle errors
Polling vs. Interrupts
Synchronous vs. Asynchronous

## Slide 3: Interrupts
What is an interrupt?
  Idea is an unsolicited procedure call.
  Actual procedure is called an exception/trap/interrupt handler
Why do we need them? Or put another way, what would we have to do if we didn’t have them?

## Slide 4: Interrupts (In generic sense)
How can interrupts be generated?
?

## Slide 5: Interrupts (In generic sense)
Different Types (2200 Definitions)
  Exception - Associated with certain instruction
    Overflow
    Illegal Instruction
  Traps – System calls (i.e. read/write file)
  Interrupt - Asynchronous event not associated with a certain instruction (e.g. I/O device).

## Slide 6: Interrupts/Exceptions/Traps
 | Synchronicity | Source | Intentional? | Example
Exception | Synch | Internal | No | Overflow, Illegal Instruction
Trap | Synch | Internal | Yes | System Call
Interrupt | Asynch | External | Yes | I/O Device Completion

## Slide 8: Dealing with Program Discontinuities
Tricky parts:
  Discontinuity can happen anywhere – i.e., in the middle of instruction execution
  Discontinuity is unplanned for and may be unrelated to the current program – i.e., hardware has to save the PC value implicitly before executing handler
  When discontinuity is detected, hardware has to determine the handler’s address
  Since PC is saved implicitly, handler has to discover how to resume normal program execution

## Slide 9: Interrupt Vector Table
Dealing with interrupts is a partnership between the processor architecture and the operating system.
What makes it possible?
A fixed-size table of handler addresses, one address for each type of anticipated interrupts (it may also handle system calls).
This table is set up at boot time

## Slide 10
Handler address
for divide by zero exception
Handler address
for arithmetic overflow
……..
Handler address
for system call trap
Handler address
for page fault trap
……..
Handler address
for KBD interrupt
Handler address
for mouse interrupt
………
Table entries for
exceptions
Table entries for
traps
Table entries for
External interrupts
0
1
n-1
.
.
.
.
.
.
.
.
Handler code for system call trap
Handler code for mouse interrupt
Handler code for divide by zero exception
Handler code for overflow exception
Handler code for page fault trap
Handler code for KBD interrupt
Interrupt Vector Table

## Slide 11: Handling Exceptions/Traps
In the case of exceptions/traps, the hardware generates the interrupt vector internally.
When exception/trap is encountered, the unique number associated with that exception/trap is placed in ETR (exception/trap register)

## Slide 12: New internal processor register
Exception/Trap number
ETR

## Slide 13: How does our state machine need to change?

## Slide 14
Fetch
Decode
Execute
INT
INT = y
INT = n
$k0 PC
PC Mem[ETR]
How Do We Need to Change FSM?

## Slide 15
Handler:
  save processor registers;
  execute device code;
  restore processor registers;
  return to original program;

## Slide 16
Handler:
save $k0;
save processor registers;
execute device code;
restore processor registers;
restore $k0;
return to original program;
Simple Handler

## Slide 17
Original program
First interrupt handler
Second interrupt handler
$ko return address for
original program
$ko return address for
first interrupt handler
How to Handle Cascaded Interrupts?

## Slide 18: Question?
Consider the following program. An interrupt occurs during the execution of ADD instruction.
100 ADD
101 NAND
102 LW
103NAND
104 BEQ
What is the PC value that needs to be preserved to resume this program after the interrupt?
100
101
102
103
104

## Slide 19: Question?
Consider the following program. An interrupt occurs during the execution of ADD instruction.
100 ADD
101 NAND
102 LW
103NAND
104 BEQ
At this time, the only registers in use by the program are R2, R3, and R4. What registers are saved and restored by the interrupt handler?
R2
R3
R4
R2, R3, R4
All the program-visible registers

## Slide 20
Fetch
Decode
Execute
INT
INT = y
INT = n
$k0 PC
PC new PC
Disable interrupts
Handling Interrupts

## Slide 21
Handler:
/* The interrupts are disabled when we enter */
save $k0;
enable interrupts;
save processor registers;
execute device code;
restore processor registers;
disable interrupts;
restore $k0;
return to original program; /* how? */
Jalr $k0 ? – interrupts have to be enabled before return
Enable interrupts
Jalr $k0
- no, new interrupt may rewrite $k0

## Slide 22
Handler:
/* The interrupts are disabled when we enter */
save $k0;
enable interrupts;
save processor registers;
execute device code;
restore processor registers;
disable interrupts;
restore $k0;
return from interrupt (RETI);
/* interrupts enabled by return from interrupt */
Interrupt Handler

## Slide 23: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2

## Slide 24: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
Add an interrupt request line. A device wishing to interrupt asserts this line

## Slide 25: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
The interrupt line is connected to the processor control (state machine)

## Slide 26: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
At the beginning of every instruction execution sequence a check is made on the status of the "int" line

## Slide 27: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
If "int" is asserted special states can be used to handle the interrupt

## Slide 28: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
If the processor decides to handle the interrupt it asserts the inta (interrupt acknowledege) line
Inta

## Slide 29: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
If Device 1 was one of the devices asserting "int" it receives the acknowledgement and doesn't pass it on
Inta

## Slide 30: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
If Device 1 wasn't one of the devices asserting "int" it receives the acknowledgement and passes it on
Inta

## Slide 31: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
Assume it's Device 2 that wants to interrupt.
Inta

## Slide 32: Interrupts
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
Now knowing that the processor is listening Device 2 can put the address of it's entry in the interrupt vector table onto the data bus
Inta

## Slide 33
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
The interrupt vector table is located in very low memory and consists of a table of pointers and stack pointers for interrupt handling routines
Inta
Memory
0x12345678
0x3579BDFA
0x12345678
0x3579BDFE

## Slide 34
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
This allows the processor to jump to the code to handle the interrupt
Inta
Memory
0x12345678
0x3579BDFA
0x12345678
0x3579BDFE

## Slide 35
Processor
Data Bus
Address Bus
Device 1
Device 2
INT
INTA
Memory
.
.
.
.
80
81
82
83
Address of handler
….
Address of handler
….
KEYBOARD
MOUSE
Interrupt vector table

## Slide 36
Processor
Data Bus
Address Bus
Device 1
Device 2
Int
Once complete the handler executes a "return from interrupt" instruction
Inta
Memory
0x12345678
0x3579BDFA
0x12345678
0x3579BDFE

## Slide 37: Questions?

## Slide 38
Processor
Device 1
Device 2
INT1
INTA 1
Device 1
Device 2
INT8
INTA 8
.
.
.
.
.
.
.
.
Priority
Encoder
INT
INTA

## Slide 39
Stack for Saving/Restoring
Where do we save processor registers?
How does handler know which part of the memory can be used by the stack?
It does not know☺
For this reason, the architecture has two stacks: user stack and system stack.
Duplicate stack pointer $sp and change FSM to perform state switching in INT macro state

## Slide 41: Arch enhancements to LC-2200

## Slide 42
1000
...
40
41
•
•
•
...
...
299
300
•
•
•
inst
inst
1000
1001
•
•
•
inst
inst
19999
20000
CONT
ADDR
Executing instruction at 19999. The PC has already been incremented. Device signals interrupt in middle of instruction. $sp points to user stack
$sp
user
stack
$k0
300
Register File
PC
20000
INT Enable
1
INT ACK
0
INT REQ
1
A.
Vector Table
System Stack
Handler Code
Original Program
MODE
USER

## Slide 43
1000
...
40
41
•
•
•
...
...
299
300
•
•
•
inst
inst
1000
1001
•
•
•
inst
inst
19999
20000
CONT
ADDR
Interrupt has been sensed. $k0 gets PC. Interrupts are disabled. Interrupt is acknowledged. Device puts vector on bus.
$sp
user
stack
$k0
20000
Register File
PC
20000
INT Enable
0
INT ACK
1
INT REQ
1
B.
Vector Table
System Stack
Handler Code
Original Program
BUS
40
MODE
USER

## Slide 44
1000
...
40
41
•
•
•
...
mode
299
300
•
•
•
inst
inst
1000
1001
•
•
•
inst
inst
19999
20000
CONT
ADDR
Handler address is put into PC;
Current mode is saved in system stack; New mode is set to kernel; $sp now points to system stack; Interrupt code at 1000 is set to handle the interrupt.
$sp
299
$k0
20000
Register File
PC
1000
INT Enable
0
INT ACK
0
INT REQ
0
C.
Vector Table
System Stack
Handler Code
Original Program
MODE
KERNEL

## Slide 45
1000
...
40
41
•
•
•
...
...
299
300
•
•
•
inst
inst
1000
1001
•
•
•
inst
inst
19999
20000
CONT
ADDR
RETI instruction restores mode from system stack; since returning to user program in this example, $sp now points to user stack; also, copies $k0 into PC, re-enables interrupts and sets Mode to User
$sp
user
stack
$k0
20000
Register File
PC
20000
INT Enable
1
INT ACK
0
INT REQ
0
D.
Vector Table
System Stack
Handler Code
Original Program
MODE
USER

## Slide 46
•
•
•
•
•
•
•
•
•
Vector Table
Handler Code
Original Program
System Stack
1000
...
40
41
...
...
299
300
inst
inst
1000
1001
inst
inst
19999
20000
CONT
ADDR
Executing instruction at 19999. The PC has already been incremented. Device signals interrupt in middle of instruction. $sp points to user stack
$sp
user
stack
$k0
300
Register File
PC
20000
INT Enable
1
INT ACK
0
INT REQ
1
A.
MODE
USER
Vector Table
Handler Code
Original Program
System Stack
1000
...
40
41
•
•
•
...
...
299
300
•
•
•
inst
inst
1000
1001
•
•
•
inst
inst
19999
20000
CONT
ADDR
Interrupt has been sensed. $k0 gets PC. Interrupts are disabled. Interrupt is acknowledged. Device puts vector on bus.
$sp
user
stack
$k0
20000
Register File
PC
20000
INT Enable
0
INT ACK
1
INT REQ
1
B.
BUS
40
MODE
USER
1000
...
40
41
•
•
•
...
mode
299
300
•
•
•
inst
inst
1000
1001
•
•
•
inst
inst
19999
20000
CONT
ADDR
Handler address is put into PC;
Current mode is saved in system stack; New mode is set to kernel; $sp now points to system stack; Interrupt code at 1000 is set to handle the interrupt.
$sp
299
$k0
20000
Register File
PC
1000
INT Enable
0
INT ACK
0
INT REQ
0
C.
Vector Table
System Stack
Handler Code
Original Program
MODE
KERNEL
1000
...
40
41
•
•
•
...
...
299
300
•
•
•
inst
inst
1000
1001
•
•
•
inst
inst
19999
20000
CONT
ADDR
RETI instruction restores mode from system stack; since returning to user program in this example, $sp now points to user stack; also, copies $k0 into PC, re-enables interrupts and sets Mode to User
$sp
user
stack
$k0
20000
Register File
PC
20000
INT Enable
1
INT ACK
0
INT REQ
0
D.
Vector Table
System Stack
Handler Code
Original Program
MODE
USER