## Slide 1: CS 2200 Memory Hierarchy

## Slide 2
Ideally one would desire an indefinitely large capacity memory such that any particular...word would be immediately available.... We are...forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.
A. W. Burks, H. H. Goldstine, and J. von Neumann
Preliminary Discussions of the Logical Design of an Electronic Computing Instrument, 1946

## Slide 3: Memory Hierarchy
Up to now…
Reality…
Processors have cycle times of ~1 ns
Fast DRAM (dynamic random access memory) has a cycle time of ~100 ns
Paging from disk is milliseconds
We have to bridge this gap for pipelining to be effective!
MEMORY
Black Box

## Slide 4: Memory Hierarchy
DRAM (Dynamic random access memory)
  Uses 1 transistor to store 1 bit
  Reading the bit depletes the charge and requires a replenishment before it can be read gain
Fast memory is possible (How?)
  Register files made of flip flops operate at processor speeds
  Such memory is Static RAM (SRAM)
  6 transistors needed for storing 1 bit, but no replenishment before reading bit again
Tradeoff
  SRAM is fast
  Economically unfeasible for large memories

## Slide 5: Memory Hierarchy
SRAM
  High power consumption
  Large area on die
  Costly per bit
DRAM
  Low power consumption
  Suitable for Large Scale Integration (LSI)
  Small size
  Ideal for large memories
  Circa 2007, a single DRAM chip may contain up to 256 Mbits with an access time of 70 ns.

## Slide 6: The Concept of a Cache
Feasible to have small amount of fast memory and/or large amount of slow memory.
Want
  Size advantage of DRAM
  Speed advantage of SRAM.
CPU
Cache
Main memory
Increasing speed as we get closer to the processor
Increasing size as we get farther away from the processor

## Slide 7: The Concept of a Cache
CPU
Cache
Main memory
Increasing speed as we get closer to the processor
Increasing size as we get farther away from the processor
CPU looks in cache for data it seeks from main memory.
If data not there it retrieves it from main memory.
If the cache is able to service "most" CPU requests then effectively we will get speed advantage of cache.
All addresses in cache are also in memory

## Slide 8
Principle of Locality

## Slide 9: Principle of Locality
A program tends to access a relatively small region of memory irrespective of its actual memory footprint in any given interval of time.
While the region of activity may change over time, such changes are gradual

## Slide 10: Principle of Locality
Spatial Locality: Tendency for locations close to a location that has been accessed to also be accessed
Temporal Locality: Tendency for a location that has been accessed to be accessed again
Example
for(i=0; i<100000; i++)
a[i] = b[i];

## Slide 11: Basic Terminologies
Hit: CPU finding contents of memory address in cache
Hit rate (h) is probability of successful lookup in cache by CPU.
Miss: CPU failing to find what it wants in cache (incurs trip to deeper levels of memory hierarchy
Miss rate (m) is probability of missing in cache and is equal to 1-h.

## Slide 12: Basic Terminologies
Miss penalty: Time penalty associated with servicing a miss at any particular level of memory hierarchy
Effective Memory Access Time (EMAT): Effective access time experienced by the CPU when accessing memory.
  Time to lookup cache to see if memory location is already there
  Upon cache miss, time to go to deeper levels of memory hierarchy
EMAT = Tc + m * Tm
where m is cache miss rate, Tc the cache access time and Tm the miss penalty

## Slide 13: Multilevel Memory Hierarchy

## Slide 14: Intel i7 Chip
L1 – 32K I / 32K D
L2 256K
L3 4-12 M

## Slide 15: Multilevel Memory Hierarchy
Modern processors use multiple levels of caches.
As we move away from processor, caches get larger and slower
EMATi = Ti + mi * EMATi+1
where Ti is access time for level i
and mi is miss rate for level i

## Slide 16
CPU
L1- cache
Main memory
L2- cache
h1 = 0.95; TL1 = 2 ns
h2 = 0.80; TL2 = 10 ns
Tm = 100 ns
EMAT?
EMAT=
TL1+(1-h1)*EMAT_12=2+0.05*(TL2+(1-h2)*Tm)=2+0.05*(10+0.2*100)=2+1.5=3.5ns

## Slide 17: Cache organization
There are three facets to the organization of the cache:
  Placement: Where do we place in the cache the data read from the memory?
  Algorithm for lookup: How do we find something that we have placed in the cache?
  Validity: How do we know if the data in the cache is valid?

## Slide 18: Direct Mapped Cache
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Given a memory address,
What is the numerical value of cache index?

## Slide 19
0
1
2
3
4
5
6
7
mem loc 0
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
Memory reference: 0, 1, 2, 3, 1, 3, 0, 8, 0, 9, 10
Cache
hits
Compulsory misses

## Slide 20
0
1
2
3
4
5
6
7
mem loc 0 8
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
Memory reference: 0, 1, 2, 3, 1, 3, 0, 8, 0, 9, 10
Compulsory miss

## Slide 21
0
1
2
3
4
5
6
7
mem loc 0 8 0
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
Memory reference: 0, 1, 2, 3, 1, 3, 0, 8, 0, 9, 10
Conflict miss

## Slide 22: How do we disambiguate?
0
1
2
3
4
5
6
7
mem loc 0 8
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
data
tag
1
0
0
0

## Slide 23: How do we know it is valid?
0
1
2
3
4
5
6
7
loc 8
loc 1
loc 2
loc 3
empty
empty
empty
empty
data
tag
1
1
1
1
valid
0
0
0
0
1
0
0
0
X
X
X
X
Valid
Tag
data

## Slide 24: Interpreting memory address
Cache Tag
Cache Index

## Slide 25: Cache Lookup
000
001
010
011
100
101
110
111
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
Cache_Index = Memory_Address mod Cache_Size

## Slide 26: Cache Lookup
000
001
010
011
100
101
110
111
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
Cache_Index = Memory_Address mod Cache_Size
Cache_Tag = Memory_Address/Cache_Size
00
00
00
00
00
00
00
00
Tag
Contents

## Slide 27: Fields of a Cache Entry
Is the sequence of fields significant?
Would this work?
Index
0000000000000000
Tag
00000000000000
Index
0000000000000000
Tag
00000000000000

## Slide 28
0
1
2
3
4
5
6
7
loc 0
empty
empty
empty
empty
empty
empty
empty
data
tag
1
0
0
0
valid
0
0
0
0
0
X
X
X
X
X
X
X
Access location 0
0
1
2
3
4
5
6
7
loc 0 1
empty
empty
empty
empty
empty
empty
empty
data
tag
1
0
0
0
valid
0
0
0
0
1
X
X
X
X
X
X
X
Access location 1
0
1
2
3
4
5
6
7
loc 0 1 0
empty
empty
empty
empty
empty
empty
empty
data
tag
1
0
0
0
valid
0
0
0
0
0
X
X
X
X
X
X
X
Access location 0
0
1
2
3
4
5
6
7
loc 0 1 0 1
empty
empty
empty
empty
empty
empty
empty
data
tag
1
0
0
0
valid
0
0
0
0
1
X
X
X
X
X
X
X
Access location 1
Cache occupancy if we switch index and tag
BAD!!

## Slide 29: Hardware for Direct Mapped Cache
y
Cache Tag
Cache Index
Valid
Tag
Data
.
.
.
.
.
.
=
hit
Data
To
CPU
Memory address

## Slide 30: Addressing Bytes in Cache

## Slide 31: Example
Let us consider the design of a direct-mapped cache for a realistic memory system.
  Assume that the CPU generates a 32-bit byte-addressable memory address.
  Each memory word contains 4 bytes.
  A memory access brings in a full word into the cache.
  The direct-mapped cache is 64K Bytes in size (this is the amount of data that can be stored in the cache), with each cache entry containing one word of data.
  Compute the additional storage space needed for the valid bits and the tag fields of the cache.

## Slide 33: Example
Number of cache entries:
64Kb/4bytes/word=16Kb entries, i.e., index=14 bits, tag=16bits
1 bit for valid bit
17bits x 16Kb=278,528 bits
Total space= 64 Kb+278,528 bits=802,816 bits

## Slide 34: Repercussion on Pipelined Processor Design
Miss on I-Cache: Insert bubbles until contents supplied
Miss on D-Cache: Insert bubbles into WB stall IF, ID/RR, EXEC
PC
I-Cache
ALU
DPRF
ALU-1
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
ALU-2
D-Cache
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data

## Slide 35: Read Access to Cache from CPU
CPU sends index to cache. Cache looks it up and if a hit sends data to CPU.
If cache says miss CPU sends request to main memory. All in same cycle (IF or MEM in pipeline)
Upon sending address to memory CPU sends NOP's down to subsequent stage until data read. When data arrives it goes to CPU and the cache.

## Slide 36: Cache read/write algorithms
Read Hit

## Slide 37: Basic cache read algorithms
Read Miss

## Slide 38: Write Access to Cache from CPU
Two choices
  Write through policy
    Write allocate
    No-write allocate
  Write back policy

## Slide 39: Write Through Policy
On each CPU write – both cache and main memory are updated
Each write goes to cache. Tag is set and valid bit is set
Each write also goes to main memory (through write buffer)
If write buffer is full at the time CPU wants to write, pipeline will stall

## Slide 40
Write-Through

## Slide 41: Write Through Policy
Write-Buffer for Write-Through Efficiency
CPU
Main memory
Address
Address
Data
Data
Address
Data
Address
Data
Address
Data
Address
Data
Write Buffer

## Slide 42: Write Through Policy
Each write goes to cache. Tag is set and valid bit is set
  This is write allocate
  There is also a no-write allocate where the cache is not written to if there was a write miss
Each write also goes to write buffer
Write buffer writes data into main memory
  Will stall if write buffer full

## Slide 43: Write back policy
We write to the cache
We don't bother to update main memory
Is the cache consistent with main memory?
Is this a problem?
Will we ever have to write to main memory?

## Slide 44: Write Back Policy
On each CPU write – only cache is updated
CPU-cache interaction same as for write-through
CPU writes data to cache setting dirty bit
  Note: Cache and memory are now inconsistent but the dirty bit tells us that
Cache clears the dirty bit upon processing a miss that brings a memory location into this cache entry
  Write buffer is used to service write miss
Cache sets the dirty bit upon a CPU write operation
The cache writes back the data into the memory upon replacement

## Slide 45
Write-Back

## Slide 46: Write Back Policy

## Slide 47: Comparison of the Write Policies
Write Through
  Cache logic simpler and faster
  Creates more bus traffic
Write back
  Requires dirty bit and extra logic
  Faster
Multilevel cache processors may use both
  L1 Write through
  L2/L3 Write back

## Slide 48: Dealing with cache misses in the processor pipeline
Read miss in the MEM stage:
I1: ld r1, a ; r1 <- MEM[a]
I2: add r3, r4, r5 ; r3 <- r4 + r5
I3: and r6, r7, r8 ; r6 <- r7 AND r8
I4: add r2, r4, r5 ; r2 <- r4 + r5
I5: add r2, r1, r2 ; r2 <- r1 + r2
Write miss in the MEM stage: The write-buffer alleviates the ill effects of write misses in the MEM stage. (Write-Through with write-allocate)

## Slide 49: Execution time with caches
Execution time = N * CPIAvg * cycle time
Execution time = N * CPIeff * cycle time
CPIeff = CPIAvg + Memory-stallsAvg
Execution time = N * (CPIAvg + M-stallsAvg) * cycle time
Memory-stallsAvg = misses per instructionAvg * miss-penaltyAvg
Total memory stalls = N * Memory-stallsAvg

## Slide 50: Example
Consider a pipelined processor that has an average CPI of 1.8 without accounting for memory stalls.
I-Cache has a hit rate of 95% and the D-Cache has a hit rate of 98%. Assume that memory reference instructions account for 30% of all the instructions executed. Out of these, 80% are loads and 20% are stores.
On average, the read-miss penalty is 20 cycles and the write-miss penalty is 5 cycles.
Compute the effective CPI of the processor accounting for the memory stalls.

## Slide 51: Example
Effective CPI= base CPI+ Effect of I-cache on CPI + Effect of D-cache on CPI=1.8+1+0.096+0.006=2.902
Base CPI=1.8
Cost of instruction misses=I-cache miss rate*read-miss penalty=(1-0.95)*20=1
Cost of data read misses=0.3*0.8*(1-0.98)*20=0.096
Cost of data write misses=0.3*0.2*(1-0.98)*5=0.006

## Slide 52: Improving cache performance
Bottom line…Improving miss rate and reducing miss penalty are keys to improving performance